## Slide 1: Alpena Biorefinery Right-To-Know / HazCom Program
“This workforce solution was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The solution was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including any information on linked sites and including, but not limited to, accuracy of the information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership.”
This work by Alpena Community College’s Sustainable Solutions for Northeast Michigan, a Department of Labor, TAACCCT funded project, is licensed under the Creative Commons Attribution 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by/4.0/

## Slide 2: Agenda
OSHA Hazard Communication Standard
MIOSHA / Right-To-Know
AB Hazard Communication Program
  Hazardous Chemicals in Use at AB
  Container Labeling Method and Policy
  Pipe Labeling Scheme
  Detecting a Release or Leak of Hazardous Chemicals
  Location of Documents Related to Right-To-Know / HazCom Program

## Slide 3: OSHA Hazard Communication Standard
Container
Labeling
Label
Hazard Communication
Program
Program
Material Safety
Data Sheet
MSDS
  OSHA Standard: 29 CFR 1910.1200
  Purpose
  To ensure that employers and employees know about work hazards and how to protect themselves so that the incidence of illnesses and injuries due to hazardous chemicals is reduced
Notes: 29 CFR 1910.1200
The Hazard Communication (HazCom) standard establishes uniform requirements to make sure that the hazards of all chemicals imported into, produced, or used in U.S. workplaces are evaluated, and that this hazard information is transmitted to affected employers and exposed employees.
The HazCom standard is different from other OSHA health rules because it covers all hazardous chemicals. The rule also incorporates a “downstream flow of information,” which means that producers of chemicals have the primary responsibility for generating and disseminating information, whereas users of chemicals must obtain the information and transmit it to their employees.

## Slide 4: OSHA Hazard Communication Standard
Basic Employer Requirements
Identify and list hazardous chemicals in their workplaces
Proper labeling of hazardous chemicals in workplaces
Maintain current Material Safety Data Sheets (MSDSs)
Develop a written hazard communication program
Implement employee hazardous chemical awareness training

## Slide 5: MIOSHA Right-To-Know Program
The state of Michigan passed Right-To-Know Law that enhances the Federal OSHA Federal Hazard Communication Standard
Compliance based on previous five requirements of Federal Standard with additional provisions

## Slide 6: MIOSHA Right-To-Know Program
Employer Requirements
Identify and list hazardous chemicals in their workplaces, including commonly used industrial products
Proper labeling of hazardous chemicals in workplaces
Proper labeling of pipe and piping systems
Maintain current Material Safety Data Sheets (MSDSs)
Develop a written hazard communication program
Implement employee hazardous chemical awareness training
Fire-Fighter Right-To-Know Law
Post the Right-To-Know Law

## Slide 7: MIOSHA Right-To-Know Program
Identify and List Hazardous Chemicals
Determination of hazardous nature done from Material Safety Data Sheets (MSDSs)
Inventory List must be developed, reviewed and updated periodically and available for employees

## Slide 8: MIOSHA Right-To-Know Program
Must also include commonly used and stored materials such as:
  Gasoline
  Diesel Fuel
  Motor Oil
  Lubricants
  Hydraulic Fluids
  Solvents
  Parts Cleaners
  Some Hand Cleaners

## Slide 9: MIOSHA Right-To-Know Program
Labeling Requirements for Containers
  Each container of hazardous chemicals entering the workplace must be marked with:
    The identity of the chemical
    Appropriate hazard warning
    Name and address of manufacturer, importer or other responsible party
    Consumer products and other chemical products subject to labeling laws of other federal agencies are exempt from labeling requirements of this standard

## Slide 10: MIOSHA Right-To-Know Program
Labeling of Consumer Products
Anything available over the counter to the general public is exempt from labeling requirements provided the item has appropriate consumer warnings on the factory label
Labeling of Stationary Process Containers
Signs, placards, process sheets, batch tickets, or other written materials can be used instead of actually affixing labels to process containers such as tanks, so long as it conveys the same information that would be put on a label and is visible to employees

## Slide 11: MIOSHA Right-To-Know Program
Labeling Portable Containers
  Not required to label portable containers that hazardous materials are transferred into from labeled containers as long as the contents are used immediately by the person who performs the transfer
  However; unlabeled containers of hazardous chemicals found in a work area may constitute a imminent danger situation
    Imminent danger means a condition or practice in a place of employment which is such that a danger exists which could reasonably be expected to cause death or serious physical harm either immediately or before the danger can be eliminated through the enforcement of procedures otherwise provided.

## Slide 12: MIOSHA Right-To-Know Program
Labeling of Pipes and Piping Systems
Employees have the right to be informed, either by label or placard, of the hazards of any chemicals in pipes or pipe systems

## Slide 13: MIOSHA Right-To-Know Program
Material Safety Data Sheets (MSDS)
Prepared by the manufacturer or importer and describe:
    Physical Hazards- fires and explosions
    Health Hazards- signs of exposure
    Routes of exposure
    Precautions for safe handling and use
    Emergency and first aid procedures
    Control measures

## Slide 14: MIOSHA Right-To-Know Program
Material Safety Data Sheets (MSDS)- cont.
  Must provide information about the:
    Physical and chemical characteristics
    Health effects
    Exposure limits
    Carcinogenicity (cancer-causing)
    Identification (name, address, phone number) of organization responsible for preparing the sheet

## Slide 15: MIOSHA Right-To-Know Program
Material Safety Data Sheets (MSDS)- cont.
  If no MSDS has been received for a hazardous chemical, employer must contact the supplier, manufacturer, or importer to obtain one and maintain a record of the contact

## Slide 16: MIOSHA Right-To-Know Program
Requirements of Written HazCom Program
  Describes container labeling, MSDSs, and employee training for each workplace
  List of hazardous chemicals and how employer will inform employees of hazards associated
  Make information regarding hazards and protective measures available to other employers onsite

## Slide 17: MIOSHA Right-To-Know Program
Training
Training is required for employees who are exposed to hazardous chemicals in their work area:
  At the time of their initial assignment
  Whenever a new hazard is introduced into their work area

## Slide 18: MIOSHA Right-To-Know Program
Training
Training must consist of the following elements:
Explanation of the HazCom Program, including information about labels, MSDSs, and how to obtain and use available hazard information
Hazards of chemicals in the work area
Protective measures such as engineering controls, work practices, and the use of PPE
How to detect the presence or release of a hazardous chemical (using monitoring devices, observation, or smell)

## Slide 19: MIOSHA Right-To-Know Program
Firefighter Right-To-Know Law
Upon request, employer must provide the fire chief with:
  Hazardous Chemical Inventory List
  MSDSs for all chemicals onsite
  Information on quantities and locations of chemicals

## Slide 20: MIOSHA Right-To-Know Program
Posting of Right-To-Know Law
  A poster must remind employees of their rights under the Michigan Right-To-Know Law and how to locate the MSDSs and RTK program.
  A second poster must inform employees of any changes recently made to one or more MSDSs
    Must be filled within 5 days of receipt of new MSDSs and must remain for a minimum of 10 days

## Slide 21: AB Right-To-Know / HazCom Program
Hazardous Chemicals Used/Produced in AB Operations
Sulfuric Acid- 93%
  Highly Corrosive
    Causes severe chemical burns upon contact
  Reacts violently with water and organic compounds
Acetic Acid
  Corrosive to skin and eyes
    Dehydrating effect on tissues
  Combustible
Potassium Hydroxide (Caustic Potash)
  Highly Corrosive
    Causes severe chemical burns that are not immediately painful
  Reacts with acids and water to produce heat
Hydrated Lime
  Strong Irritant
    Eye contact can cause burns and permanent damage
    Skin contact particularly in the presence of moisture

## Slide 22: AB Right-To-Know / HazCom Program
Hazardous Chemicals Used/Produced in AB Operations
Gasoline (Denaturant)
  Highly Flammable Liquid
    Vapors can form explosive mixtures with air
Ethanol
  Highly Flammable Liquid
    Vapors can form explosive mixtures with air
Sodium Hydroxide (Caustic Soda)
  Highly Corrosive- slightly less than KOH
    Causes severe chemical burns that are not immediately painful
  Reacts with acids and water to produce heat

## Slide 23: AB Right-To-Know / HazCom Program
  Reducing or Preventing Exposure to Hazardous Chemicals
  By using the Hierarchy of Controls AB will try to minimize the risk of injury from hazardous chemicals

## Slide 24: AB Right-To-Know / HazCom Program
  Reducing or Preventing Exposure to Hazardous Chemicals
  Elimination
    Where possible, the use of hazardous chemicals has been avoided
      However, in order to execute the process and achieve the desired ethanol product, chemicals such as sulfuric acid and potassium hydroxide must be used

## Slide 25: AB Right-To-Know / HazCom Program
  Reducing or Preventing Exposure to Hazardous Chemicals
  Substitution
    When possible, the substitution of less hazardous or non-hazardous chemicals have been chosen
      After hydrolysis, neutralization is required. Hydrated lime will be used for this, which is a moderate skin irritant but not immediately corrosive to skin

## Slide 26: AB Right-To-Know / HazCom Program
  Reducing or Preventing Exposure to Hazardous Chemicals
  Modification
    At some sample locations, modifications to sample valves have been or will be made to contain or cool the material to reduce exposure risk
    One or two sample points have also been moved to a different locations to lessen the hazard of sample collection

## Slide 27: AB Right-To-Know / HazCom Program
  Reducing or Preventing Exposure to Hazardous Chemicals
  Ventilation
    In the Fermentation area, a CO2 scrubber is in place to remove CO2 gas from the process and ventilate it to the atmosphere where does not present a hazard

## Slide 28: AB Right-To-Know / HazCom Program
  Reducing or Preventing Exposure to Hazardous Chemicals
  Containment
    In the Hydrolysis Reactor area, containment curtains will be installed to cordon off the area to prevent sudden exposure to highly dangerous material should a leak occur

## Slide 29: AB Right-To-Know / HazCom Program
  Reducing or Preventing Exposure to Hazardous Chemicals
  Work Practices
    The practice of completing a hazard assessment and permit to enter a confined space ensures that all hazards related to the chemicals in use are recognized and addressed prior to entering
    The practice of limiting the circumstances that require AB employees to enter a confined space reduces exposure

## Slide 30: AB Right-To-Know / HazCom Program
  Reducing or Preventing Exposure to Hazardous Chemicals
  PPE
    When in the Reactor Area, or Fermentation Area when CIP light is flashing, additional PPE is required to prevent exposure to the hazardous chemical in use
    Specific sampling locations and procedures also require additional PPE based on the characteristics of the sample to be taken

## Slide 31: AB Right-To-Know / HazCom Program
Container Labeling Policy and Methodology
  It will be the responsibility of the person receiving a material to verify that containers are clearly labeled with the following:
    The contents of the containers
    The appropriate hazard warning
    The manufacturer’s name and address

## Slide 32: AB Right-To-Know / HazCom Program
  Container Labeling Policy and Methodology
  It will be the responsibility of the person who is placing and/or using a material in a secondary container to ensure the container is labeled either by:
    An extra copy of the original manufacturer’s label with hazard warning
    NFPA Hazard Diamond designation and chemical identification

## Slide 33: AB Right-To-Know / HazCom Program
  Container Labeling Policy and Methodology
    Example- Sulfuric Acid
3
COR
1
0
Sulfuric Acid
CHEMICAL
Jacey Radel 03/19/2012
OWNER DATE

## Slide 34: AB Right-To-Know / HazCom Program
  Pipe Labeling Scheme
    All piping systems will be marked with a colored label using the following ANSI A13.1-2007 recommendations for line coloration
Color Designation
Fire Quenching Fluids White on Red
Toxic & Corrosive Fluids Black on Orange
Flammable Fluids Black on Yellow
All Water and Non-Hazardous Process Fluids White on Green
Compressed Air White on Blue

## Slide 35: AB Right-To-Know / HazCom Program
  Pipe Labeling Scheme
  The color of the label will denote specific hazards associated with the material in the line
    Additional hazards may be present in the material and will be listed after the name of the material
SULFURIC ACID - HOT

## Slide 36: AB Right-To-Know / HazCom Program
  Detecting a Release or Leak of Hazardous Chemicals
  Alarms from pressure, temperature, and level indications on lines and tanks throughout the process may remotely signal a release or leak
  Pooling of material, or fluid dripping/spraying from pipes or valves will visually indicate a leak or release
  Leaks in pressurized systems may also be detected by sound. Caution – Dangerous leaks may not be visible

## Slide 37: AB Right-To-Know / HazCom Program
  Detecting a Release or Leak of Hazardous Chemicals
    If release or leak is encountered, the line must be shutdown remotely if possible
    Do not risk personal safety in investigating a release or leak
    If it must be done manually, additional PPE and caution will likely be required to avoid injury

## Slide 38: AB Right-To-Know / HazCom Program
  Location of Documents Related to Right-To-Know / HazCom Program:
    In the Control Room the following hard copies will be located:
      The Right-To-Know / HazCom Written Program
      MSDSs for all chemicals on-site
    Both will also be electronically filed in the W: Drive
      Safety Folder
        RTK / HazCom Program