## Slide 1: Blueprint Reading
Section II - Sketching

## Slide 2: Disclaimer
The AMMQC program is an Equal Opportunity program. Adaptive equipment is available upon request for individuals with disabilities. http://creativecommons.org/licenses/by/3.0 This work is licensed under a Creative Commons Attribution 3.0 Unported License [http://creativecommons.org/licenses/by/3.0] This project is sponsored by a $15.9 million grant from the U.S. Department of Labor, Employment and Training Administration. The AMMQC program is an Equal Opportunity program. Adaptive equipment is available upon request for individuals with disabilities. This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including any information on linked sites and including, but not limited to, accuracy of the information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership.

## Slide 3: Why Sketching?
Known as the “Universal Language”
Fast, Visual Communication
  Pictures are worth a thousand words
Documentation
Notes: Design for a Giant Crossbow - Leonardo Da Vinci. Digital image. Wikipaintings.org. N.p., n.d. Web. 9 Aug. 2013. <http://www.wikipaintings.org/en/leonardo-da-vinci/design-for-a-giant-crossbow-1482#supersized-artistPaintings-225127>.
Sketches can be considered the “Universal Language” because a sketch in Japanese can still be interpreted fairly well by an American.
Tank Sketch - Leonardo Da Vinci. Digital image. Bbc.com.uk. N.p., n.d. Web. 9 Aug. 2013. <http://www.bbc.co.uk/history/worldwars/wwone/images/tank_image1.jpg>.
Sketches do not have to be “perfect”, just quick and clear. Small job shops sometimes use sketches as the formal production drawing.
Sketches can document existing conditions for use in reports or be used to illustrate ideas and concepts.
Shown are Leonardo da Vinci’s crossbow and tank designs

## Slide 4: Sketching Techniques
Sketching a straight line

## Slide 5: Drawing Direction
To the right and down – right handed
To the left and down – left handed
Right Handed
Left Handed

## Slide 6: 2 Methods – Straight Line
Light, Short Strokes
Dot to Dot
Long Strokes Cause Problems
Notes: Two methods to draw a straight line
Light short strokes 2 to 3 inches long then darken it in
Dot to Dot
If you try to draw a long stroke it will typically cause the line to curve

## Slide 7: Use an Edge
Try using the edge of the paper

## Slide 8: Practice! Practice!
Practice drawing a series of lines of different lengths vertically 1” through 6” in approximately 1” increments
Do the same horizontally
Draw a star
  Hint: Turn the paper while you draw
Speed does not equal accuracy

## Slide 9: Drawing a Circle – Method 1
Lightly draw a square the same size as circle

## Slide 10: Drawing a Circle – Method 1 #2
Lightly draw diagonal lines corner to corner
Lightly mark approximately where the radius goes

## Slide 11: Drawing a Circle – Method 1 #3
Draw the circle touching each side of the square and passing through each radius point

## Slide 12: Drawing a Circle – Method 2
Lightly draw lines as shown,
slightly bigger than the circle

## Slide 13: Drawing a Circle – Method 2 #2
Mark radius points as shown

## Slide 14: Drawing a Circle – Method 2 #3
Connect the dots

## Slide 15: Drawing a Circle – Method 3
Trammel Method
Notes: Use a piece of paper and mark the radius of the circle (AB)
Lightly draw one centerline
Hold point B and place the pencil tip at point A
Use the piece of paper with the radius as a “compass” and draw the circle lightly
Darken the circle

## Slide 16: Drawing Arcs
Use the same method as a circle,
except only part of the circle is drawn

## Slide 17: Drawing Ellipses
The anatomy of an ellipse

## Slide 18: Drawing Ellipses #2
Lightly layout lines as shown

## Slide 19: Drawing Ellipses #3
Mark radii

## Slide 20: Drawing Ellipses #4
Connect the dots

## Slide 21: Practice! Practice!
Practice drawing
  A 2” circle using each method
  A 2” donut with a 1” center
  A wheel with spokes, any size
  Two ellipses of different sizes

## Slide 22: Measurement Lines
Sketch lines are related by size and direction
For the sketch to be accurate it also needs proportion
Proportion is more important than size
Notes: Looking at Line 1 and Line 2 ask these questions:
Are the two lines the same length? Obviously not.
If Line 2 is longer than Line 1, how much longer is it? Answer: twice as long. This is proportion.
What is the direction and position of the Lines? Answer: they are parallel.

## Slide 23: Measurement Lines #2
Measurement Lines allow you to setup the “Proportion” of the sketch

## Slide 24: Measurement Lines #3
This allows a proportional space to be created

## Slide 25: Blocking Technique
“Blocked” sketches
Notes: The “Block” defines the outline of the sketch and everything is drawn within it. It is drawn as a very light rectangle.

## Slide 26: Blocking Technique #2
“Blocked” sketches
Notes: The object starts with two measurement lines and a rectangular box is sketched in to the right proportion
Then additional light construction lines are added and then cleaned up to be the object

## Slide 27: Blocking Technique #3
“Blocked” sketches
Notes: The object starts with two measurement lines and a rectangular box is sketched in to the right proportion
Then additional light construction lines are added and then cleaned up to be the object

## Slide 28: Blocking Technique #4
“Blocked” sketches
Notes: The object starts with two measurement lines and a rectangular box is sketched in to the right proportion
Then additional light construction lines are added and then cleaned up to be the object

## Slide 29: Creating a Multi-View Sketch
Notes: The pictorial to the left is the given object, it is shown in an isometric view. We want to show the 3 views (orthographic projection) of this object by sketching it. More on orthographic and isometric projection later.

## Slide 30: Creating a Multi-View Sketch #2
Notes: The pictorial to the left is the given object, it is shown in an isometric view. We want to show the 3 views (orthographic projection) of this object by sketching it. More on orthographic and isometric projection later.
Step 1 is to rough in the rectangles for each view as shown
Step 2 is to add all the construction lines
Step 3 is to clean up lines not needed

## Slide 31: Creating a Multi-View Sketch #3
Step 1
Notes: The pictorial to the left is the given object, it is shown in an isometric view. We want to show the 3 views (orthographic projection) of this object by sketching it. More on orthographic and isometric projection later.
Step 1 is to rough in the rectangles for each view as shown
Step 2 is to add all the construction lines
Step 3 is to clean up lines not needed

## Slide 32: Creating a Multi-View Sketch #4
Step 2
Notes: The pictorial to the left is the given object, it is shown in an isometric view. We want to show the 3 views (orthographic projection) of this object by sketching it. More on orthographic and isometric projection later.
Step 1 is to rough in the rectangles for each view as shown
Step 2 is to add all the construction lines
Step 3 is to clean up lines not needed

## Slide 33: Practice! Practice!
Practice drawing – 15 minutes
  Make a front, right and top view of the capital letters E, F, H, I, O, and Z make them approximately 3” high and 2” wide
Notes: As time permits

## Slide 34: Creating a Isometric Sketch
Notes: Simple Isometric axis shown
Object drawn along the axis looks like this
Notice the 30 degree angle for the corners

## Slide 35: Creating a Isometric Sketch #2
Notes: Simple Isometric axis shown
Object drawn along the axis looks like this
Notice the 30 degree angle for the corners

## Slide 36: Creating a Isometric Sketch #3
Notes: Simple Isometric axis shown
Object drawn along the axis looks like this
Notice the 30 degree angle for the corners

## Slide 37: Practice! Practice!
Practice drawing – Homework
  Make an isometric view of the capital letters E, F, H, I, O, and Z make them approximately 3” high and 2” wide and 1” deep
Notes: As time permits

## Slide 38: Credits
Unless indicated otherwise all images are from Madsen, David A., and David P. Madsen. Print Reading for Engineering and Manufacturing Technology. Clifton Park, NY: Delmar, Cengage Learning, 2013. Print.