## Slide 1: Blueprint Reading
Section VIII – Fasteners and Springs

## Slide 2: Disclaimer
The AMMQC program is an Equal Opportunity program. Adaptive equipment is available upon request for individuals with disabilities. http://creativecommons.org/licenses/by/3.0 This work is licensed under a Creative Commons Attribution 3.0 Unported License [http://creativecommons.org/licenses/by/3.0] This project is sponsored by a $15.9 million grant from the U.S. Department of Labor, Employment and Training Administration. The AMMQC program is an Equal Opportunity program. Adaptive equipment is available upon request for individuals with disabilities. This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including any information on linked sites and including, but not limited to, accuracy of the information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership.

## Slide 3: Standards….
Notes: There are many standards governing fasteners, springs and other hardware

## Slide 4: External Threads
Notes: External threads and the terminology associated with it.
We are only interested in the Major Diameter and the number of threads per inch

## Slide 5: Internal Threads
Notes: Again we are only interested in the Major Diameter of the thread and the number of teeth per inch.

## Slide 6: Reading a Thread Note (Inch)
1/2 - 13 UNC-2A
The major diameter
Number of threads per inch
Class
Of
Thread
fit
Type
Of
thread
Notes: Common:
UNC = Unified National Course
UNF = Unified National Fine
Uncommon:
UNEF = Unified National Extra Fine
UNS = Unified National Special
Class of thread:
1 = Large tolerance
2 = General tolerance
3 = Tight tolerance
A = External
B = Internal
A or B does not have to be shown if it’s obvious which one it is.

## Slide 7: Reading a Thread Note (MM)
Type
Of
thread
M 10 x 1.5-6H
The major diameter
Number of threads per inch
Class
Of
Thread
fit
Notes: M is the ISO standard for metric thread and is always shown
The Major Diameter is listed in millimeters
The thread pitch is listed in millimeters
The number can be 3 thru 9 which identifies the grade of tolerance from fine to course
The letter is uppercase for internal threads and lower case for external threads. The higher the letter, the tighter the tolerance. 6H is approximately the same as 2B in the inch system.

## Slide 8: Thread Representation
Notes: Threads can be shown many different ways, depending on application.

## Slide 9: Bolt Types

## Slide 10: Machine Screw Types

## Slide 11: Cap Screw Types

## Slide 12: Nut Types

## Slide 13: Set Screws

## Slide 14: Pipe Threads
Notes: Just a representation of pipe threads. Notice the taper.

## Slide 15: PEM
Notes: PEM (brand name) self-clinching fasteners
Self-clinching nut
Self-clinching standoff
Self-clinching stud

## Slide 16: Common Washers

## Slide 17: Dowels

## Slide 18: Taper Pins

## Slide 19: Other Pin Types

## Slide 20: Snap or Retaining Rings

## Slide 21: Key Types

## Slide 22: Rivets

## Slide 23: Springs
Notes: Too many spring types to show

## Slide 24: Cone Washers
Notes: Typically called Belleville washers because they are the major manufacturer.
These can substitute for springs and are used in compression situations.

## Slide 25: Credits
Unless indicated otherwise all images are from Madsen, David A., and David P. Madsen. Print Reading for Engineering and Manufacturing Technology. Clifton Park, NY: Delmar, Cengage Learning, 2013. Print.