## Slide 1: Direct and Alternating Current

## Slide 2: Disclaimer
The AMMQC program is an Equal Opportunity program.
Adaptive equipment is available upon request for individuals with disabilities.
http://creativecommons.org/licenses/by/3.0 This work is licensed under a Creative Commons Attribution 3.0 Unported License [http://creativecommons.org/licenses/by/3.0]
This project is sponsored by a $15.9 million grant from the U.S. Department of Labor, Employment and Training Administration.
The AMMQC program is an Equal Opportunity program. Adaptive equipment is available upon request for individuals with disabilities. This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including any information on linked sites and including, but not limited to, accuracy of the information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership.

## Slide 3: ELECTRICITY

## Slide 4: DIRECT CURRENT

## Slide 5: ALTERNATING CURRENT

## Slide 6: DC - VOLTAGE
Volts +
0
Time (sec.)
Voltage remains constant

## Slide 7: AC - CYCLES
Volts +
Volts -
0
Time (sec.)
1 cycle
AC DC Video
Voltage fluctuates

## Slide 8: AC - FREQUENCY
Volts -
0
Time (sec.)
Volts +
1 cycle
Frequency = number of cycles per second
Measured in Hertz (Hz)
1Hz = 1 cycle per second

## Slide 9: AC - PEAK VOLTAGE - V0
Peak Voltage (V0) = highest voltage value in either + or - direction
Volts -
0
Volts +
1 cycle
Peak (+) voltage
Peak (-) voltage
Peak to Peak voltage

## Slide 10: AC - RMS VOLTAGE - Vrms
Root Mean Square voltage (Vrms) is an average voltage
Vrms = V0 / √2 = V0 x .707
Volts -
0
Volts +
Peak (+) voltage
Peak (-) voltage
RMS voltage

## Slide 11: FLOW OF CURRENT VS ELECTRONS
Current is considered to flow from + to –
This convention was adopted prior to fully understanding the atom and the flow of electrons

## Slide 12: INTRO VIDEO
https://www.youtube.com/watch?v=EJeAuQ7pkpc