## Slide 1: Lean Manufacturing
Presentation by David O. Hunt, PE

## Slide 2: The AMMQC program is an Equal Opportunity program. Adaptive equipment is available upon request for individuals with disabilities. http://creativecommons.org/licenses/by/3.0 This work is licensed under a Creative Commons Attribution 3.0 Unported License [http://creativecommons.org/licenses/by/3.0] This project is sponsored by a $15.9 million grant from the U.S. Department of Labor, Employment and Training Administration. The AMMQC program is an Equal Opportunity program. Adaptive equipment is available upon request for individuals with disabilities. This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including any information on linked sites and including, but not limited to, accuracy of the information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership.

## Slide 3: OBJECTIVES
Describe the history of Lean Manufacturing and how Lean Manufacturing differs from traditional assembly lines.
Explain the rationale for and effectiveness of the Lean approach, and how it reduces waste.
Use and interpret a value stream map.
Recognize and understand the language of and some key tools of Lean Manufacturing, including Gemba, Poke Yoke, 5W-2H, 5S, Kaizen, the Seven Wastes.
Through videos and exercises, “learn to see” where waste is in a process.
Describe the DMAIC process and how it relates to reducing waste.

## Slide 4: Lean: What is it?
Lean is a process of continually improving how you do things to be more efficient, lower cost, and faster
Lean is about maximizing operations the customer will pay for, and minimizing or eliminating everything else
Lean is far, far more than just saving money
Lean is not a “flavor of the month” program to be implemented willy-nilly
Lean is a philosophy that needs to be rooted in the corporate culture and led/promoted from the top
  Or it just won’t work

## Slide 5: Why Implement Lean?
Companies compete on four axes:
  Cost
  Quality
  Function
  Speed / Agility

## Slide 6: Why Implement Lean? (continued)
Reduce costs
Improve quality
Become efficient
Rapidly respond to customers
Increase profits

## Slide 7: A Brief History
Source: http://www.strategosinc.com/lean_manufacturing_history.htm

## Slide 8: From Ben Franklin…
'Buy what thou hast no need of, and ere long thou shalt sell thy necessaries.‘ (Poor Richard’s Almanac)
Translation: Don’t buy – or do – what you don’t need to do.
This, really, is the heart of Lean:
  Maximize operations that the customer is willing to pay for
  Minimize (or eliminate) everything else

## Slide 9: Henry Ford and others
Ford standardized many processes
The assembly line required standardized (and interchangeable) parts
Was still a “push process” not a “pull process”
What is the difference? Let’s go to a video…
https://www.youtube.com/watch?v=DoXE_lX3Zzo

## Slide 10: Concept: Push vs. Pull
Push:
  Making parts to a scheduled or predicted demand, not to an actual demand
  Not very adaptive to shifts in demand mix
Pull:
  Making product only when demanded by the customer
  Build to order & ship
    When demand / mix are stable and even
  Build to replenish stock when orders are shipped
    When demand / mix are unstable

## Slide 11: More History
Toyota Production System
  Post WWII Japan
  Recognized that work should be based on orders, not pre-determined targets
    I.e., PULL not PUSH
  Taichii Ohno, Shigeo Shingo were the main players at Toyota
    Ohno actually watched Ford’s assembly lines to learn
  Deming, Juran, Ishikawa – look them up
    Many good materials on-line
  Added in a focus on quality and employee involvement

## Slide 12: Modern Day
James Womack
  Book: “The Machine that Changed the World”, 1990
Many companies try
Not as many succeed
Why?
  Lean is a culture, not a program-of-the-month
  It must come from the top, who show their commitment
  It requires involvement of hourly employees
  It requires trust, going both ways
It’s the mentality… not the raw dollars (A study in tea)

## Slide 13: Mindset, Not Just Dollars: Tea Time
At Toyota, two cafeteria workers noticed they were discarding a lot of tea after lunch
They gathered data
  Recorded waste amounts, which tables, when occupied, etc.
Ran experiments testing their theories
Discovered:
  Tables nearer windows were more popular
  Filled carafes accordingly
  Virtually eliminated wasted tea
Result: Awarded Toyota’s highest honor
“Mind the pennies and the dollars will take care of themselves”

## Slide 14: Lean: Not Utopia
There is no “cookie cutter” approach to Lean
One size does not fit all
Guidelines are just that – guidelines
  Must be customized / adapted to the circumstance
Always keep in mind:
  The leaner you get the more susceptible to “Murphy” you become. (He’s out there, and he’s an SOB.)
  Any Lean program must be balanced against the customer’s Pissed-Off Factor (POF)

## Slide 15: And So It Begins…
First, a video
This video highlights many of the wastes that Lean combats
This is a two-fer:
  Once before you’ve learned anything
  Then again afterwards
You must learn to see
Test_ExportFile_IRT_Master_2016_Industry Readiness Training Post-Test.zip

## Slide 16: Discussion
What wastes did you see?

## Slide 17: The Seven Wastes
There is an acronym: TIM WOOD
T: Transportation
I: Inventory
M: Motion
W: Waiting
O: Overprocessing
O: Overproduction
D: Defects

## Slide 18: TIM WOOD – Transportation
Moving parts hither and yon
For example, one functional area (molding), to another (assembly)
  Instead of flowing on a product-focused layout
  But this, too, can be taken to an extreme
Moving things into and out of inventory / storage
Moving things to get them out of the way
Not using transportation’s capacity (e.g., a half-filled large truck)
Not for nothing are drawings of material flow in a facility often called a “spaghetti diagram”

## Slide 19: TIM WOOD – Inventory
Inventory is a carried cost; money is paid but revenue not yet realized
Building to inventory means you’re building things that haven’t been sold yet
Minimize inventory – does not mean eliminate inventory
  Remember the customer’s POF
Ties up space that could be used

## Slide 20: TIM WOOD – Motion
Motion itself is necessary
What is not necessary
  Looking for things
  Handling something multiple times
  Going to get something you should have readily available
  Having to look for instructions on how to do a task

## Slide 21: TIM WOOD – Waiting
Waiting for parts or tools needed to do your job
Waiting idle while a machine cycles
Waiting for approvals
  Or for repairs
  Or an answer to a question
  Or for the computer to catch up with you
This does not need to be a person waiting
  Machines can be idle too
  Critical if this is a constraint (bottleneck) operation

## Slide 22: TIM WOOD – Overprocessing
Simply put: Doing more than necessary
Overengineering a product
Unnecessary / unwanted features
Processing for longer than necessary

## Slide 23: TIM WOOD – Overproduction
Making more than is needed
This actually impacts almost every other kind of waste!
  Has to be stored
  Ties up money
  Defects require more sorting
  Has to be moved around more

## Slide 24: TIM WOOD – Defects
Cost of scrapped material & labor
Waste of a constraint operation
Rework costs labor $
  And if done by production people diverts them from production!
Slows reaction time to the customer
Repair areas require additional (unnecessary) tools

## Slide 25: Toast!
Now that we’ve gone over TIM WOOD, let’s revisit… TOAST!
https://www.youtube.com/watch?v=CJSZj9bShAI
What did you see this time?

## Slide 26: Seeing Again
Here’s another video
https://www.youtube.com/watch?v=dLhWoa-TmJY
The video showed types of waste
Did you see any other wastes that weren’t mentioned?
Did you notice something at the end?

## Slide 27: The Kano Quality Model

## Slide 28: Kano Quality Levels (1 of 3)
Basic characteristics: the minimum required
Presence is expected
Absence is noticed
For example: A New Car
  Starts
  No squeaks / rattles
  All the gizmos work

## Slide 29: Kano Quality Levels (2 of 3)
Performance Characteristics
“More is better”
E.g., a new car
  Fast power windows
  Really good sound system
  Good gas mileage

## Slide 30: Kano Quality Levels (3 of 3)
Value-Added Characteristics
“Surprise and delight”
E.g., a new car
  Voice-actuated climate control
  Twin sun visors
Often these can be amazing, but…
New and different can also backfire

## Slide 31: Why does the Kano Model Apply?
If you’re buying, you want you to compete purely on cost
If you’re selling, you want to compete on function and quality and speed
Being able to provide extra value to the customer enables differentiation

## Slide 32: Glossary
Autonomation or Jidoka
Benchmarking
Blitz
Cycle Time
Five S (5S)
Flow
Gemba
Genchi Genbutsu
Heijunka
Just-in-Time (JIT)
Kaikaku
Kaizen
Lead Time
Muda
Mura
Muri
Pokayoke
Pull
Push
Takt Time
Value
Value Stream Map

## Slide 33: Tools: 5S
5S is a series of “S” words used to help streamline an area
It’s not just about housekeeping
  Though neatness and organization counts
It’s about processes and discipline
Done by the workers themselves
  Instills pride

## Slide 34: What are the 5 S’s?
Sort: Sort out & separate that which is needed & not needed in the area.
Straighten: Arrange items that are needed so that they are ready & easy to use. Clearly identify locations for all items so that anyone can find them & return them once the task is completed.
Shine: Clean the workplace & equipment on a regular basis in order to maintain standards & identify defects.
Standardize: Revisit the first three of the 5S on a frequent basis and confirm the condition of the Gemba using standard procedures.
Sustain: Keep to the rules to maintain the standard & continue to improve every day.

## Slide 35: 5S: A Practical Example
Let’s go to a video
https://www.youtube.com/watch?v=hagc33G0oOg
What did you see?
Was this practical advice you can use?

## Slide 36: Taking the First Step
Before you know how to get somewhere…
You need to know where you are
In Lean Manufacturing, this means creating a Value Stream Map
A Value Stream Map is a map of what happens now
It requires an honest assessment of the present reality
It requires a multiplicity of eyes with different perspectives

## Slide 37: What does it look like?

## Slide 38: How to do one?
Start by examining your product volumes
Classify them into families, e.g.:
  Large products
  Small products
Pick a “typical” representative of each family
Walk the product from soup to nuts
  From when a customer places an order…
  To when it’s loaded on a truck

## Slide 39: And Start Drawing: Symbols

## Slide 40: Step By Step
Map the actual process
  Thinking high-level (at least at first)
  Danger: Can get caught in the weeds
Follow the parts through from beginning to end
  Can go forward or backwards through the flow
Take notes. Lots of notes.
  This is an application of “go and see”, or Genchi Genbutsu
  Get real data, nothing preprocessed
Critical: Talk with the workers!

## Slide 41: VSMs: There will be pushback
Doing a VSM is not a trivial exercise
Lots of time on the floor not doing “what you should be doing”
Lots of disturbing/distracting with many questions
Lots of poking around
Lots of information gathering
Doing it right is a pain in the you-know-where

## Slide 42: Add In Process Data
Inventory amounts
Cycle time (time taken to make one product)
Change over time (from last good piece to first good piece)
Up-time (on-demand machine utilization)
Number of operators
Shifts worked
Net available working time
Scrap rate
Pack size/pallet sizes
Batch Size
TAKT time

## Slide 43: Look for Inventory & WIP
Inventory and WIP and commonplace
  Neither cannot be totally eliminated
But is all that WIP really necessary?
Inventory and WIP are often used as a cushion to hide problems
Inventory and overproduction are two wastes
Balance WIP minimization against the POF

## Slide 44: Add In Timelines
How long are parts waiting to be moved?
How long does it take them to travel to where they are used?
How long are they stored waiting to be processed?
How long does the cycle time take?
Lather, rinse, repeat through the whole chain, operation to operation, to the end

## Slide 45: Take Notes, Talk with People
Take notes on what you see
Take lots of notes
Talk with people
  What pisses them off?
  What prevents them from being more efficient?
  Look for PITAs (Pains In The A--)
  Ask open-ended questions… WHY, WHERE, WHAT, WHO, WHEN, HOW
    As a team develop a stock slate of questions

## Slide 46: Analyze the VSM
Questions to ask include:
  How much time is spent idle vs. being processed?
  How long do parts sit in inventory?
  Cycle times vs. TAKT times?
  Poor quality – being hidden by WIP?
  Long set-up times?
  Is this step adding value?
One thing a VSM is NOT…
  A physical flow of material through the facility

## Slide 47: Don’t Be Afraid to Sit & Stare
Once a VSM is done and everyone’s happy…
Invite people to look at it
  Get them to write down their observations
  And suggestions for improvement
  Not just office people, but floor personnel
Don’t rule out just sitting and staring at it
Your subconscious is very powerful

## Slide 48: Now… Create the Future
TIM WOOD
  Analyze / ask about each step
Be systematic
You want to nitpick
  Create lots of potential projects
  Think “What if…” and “If only…”
  Imagination first, then figure out how to implement

## Slide 49: The VSM Process is…
Iterative
  You will not be able to make all the changes you seek at once
  Focus on “low hanging fruit”
  Start small; small wins encourage more effort
  Successes build on successes – success is contagious
A learning process
  Don’t be discouraged if things don’t go as planned
  “Either I win or I learn” – proverb from the internet

## Slide 50: The LEGO Game
We’re going to do an exercise
You are the production and supervisory personnel
You will be producing assemblies
The first time will be a “push” process
Then… you get to make suggestions on improving the process

## Slide 51: LEGO Game: Take 1
Just do it!

## Slide 52: The LEGO Game: Debrief
What did you observe?
Let’s walk through TIM WOOD on the board
  Transportation
  Inventory
  Movement
  Waiting
  Overproduction
  Overprocessing
  Defects

## Slide 53: The LEGO Game (Again)
Brainstorm suggestions to improve

## Slide 54: LEGO Game: Take 2
Just do it!

## Slide 55: LEGO Game Debrief
Discuss results
  What did you observe?
  Were things better? Faster?
  TIM WOOD – how’d he do?

## Slide 56: Process, Not Goal
Lean focuses on processes, not goals
Get the process right, the goals will take care of themselves
  Process improvements do include goals
E.g., losing weight / getting fit
  Those who set a goal (e.g., lose 20 pounds) will almost surely backslide
  Those who change their lifestyle (process) will be more successful

## Slide 57: Tools: Kaizen / Kaizen Blitz
Kaizen: Continuous Improvement
  Always be tweaking
  Always be looking for new ways to do things
  Small changes are easier to make
  Constant churn of ideas
Kaizen blitz: Improving a specific thing with an intense focused effort
  Specific
  Targeted
https://www.youtube.com/watch?v=su9CulCZTBg

## Slide 58: Other Tools: SMED
Single Minute Exchange of Dies
What does this really mean?
  Rapid changeover from one product to another
Reduced set-up times
Facilitates smaller batch sizes
Lowers inventory
But… it takes discipline

## Slide 59: DMAIC
Define: Describe the problem, who will work on it, and what the goals are
Measure: Go out and measure what’s happening now
Analyze: Crunch the data, understand WHY
Improve: Make changes, check results
Control: Maintain the gain

## Slide 60: Creating a Lean Enterprise (1 of 4)
The customer is the starting and ending point.
Think simplicity.
Reduce or remove waste.
Think in terms of process.
Increase visibility and transparency wherever possible.

## Slide 61: Creating a Lean Enterprise (2 of 4)
Encourage routine and standardization.
Make flow as constant and smooth as possible.
Pull at the customer’s rate, rather than pushing product through.
Get the timing right.
Be proactive and preventative rather than reactive.

## Slide 62: Creating a Lean Enterprise (3 of 4)
Keep production and process timelines as short as possible.
Make continuous improvement a priority for everyone.
Encourage internal and external players to be partners rather than competitors.
Create a supply chain that creates value.
Remember Gemba.

## Slide 63: Creating a Lean Enterprise (4 of 4)
Reduce variation where possible.
Encourage participation and accountability from all employees.
When making changes, start with the smallest component and build up.
Build trust internally and externally.
Build and distribute knowledge throughout the organization.

## Slide 64: Summing Up
Lean Manufacturing is about competition
  Speed
  Quality
  Cost
Companies that improve will survive
Companies that don’t… won’t